## Slide 1: Robotic Arm
Valeriya Khan Dias Issa
Nurbolat Sagitzhan Raiymbek Mustazhapov

## Slide 2: Idea
Original idea to combine sensors, servo motors and hydraulic arm
Using medical syringes as a hydraulic medium construct light-weight arm
Syringes are expanded/contracted by motors
Motors are controlled by sensors
Affordable design

## Slide 3: Used Materials
4 Servo Motors
8 Medical 10ml Syringes
1 Arduino Uno board
5 Flex Sensors
Cardboard
Water
Glue, Toothpicks and other materials

## Slide 4: Implementation: Cardboard
Cardboard Arm
4 dynamic parts
  Foundation - rotation of whole arm (approx. 75)
  Lower Bone – up/down moves
  Upper Bone – up/down moves of gripper
  Gripper – catch/release objects

## Slide 5: Implementation: Hydraulics
Lynxmotion Vacuum Gripper Kit
4 syringes to control 4 dynamic parts
4 servo motors
Conversion of rotational move to linear move

## Slide 6: Implementation: Circuits
Arduino Uno Board
Analog Inputs for Flex Sensors
Digital Pins for Servo Control
5 flex sensors
8 states:
Combination of 1 sensor with other 4

## Slide 7: Implementation: Code
Arduino’s servo.h library used
Calibration Part
First 100 values read
Average working value of sensors
Implementation Part
  Every 100th average read to avoid bouncing

## Slide 8: Difficulties
Power: not enough
Sensor values: as always holy mess
Coding challenge: choosing method, concurrency
Design and assembly: symmetry and calibration of positions (syringes)

## Slide 9: Results
Video 1
Video 2

## Slide 10: Thanks for attention!

## Slide 11: Reference
http://www.lynxmotion.com/p-825-vacuum-gripper-kit-with-wrist-rotate.aspx
https://www.youtube.com/watch?v=P2r9U4wkjcc&t=285s